Sketch of the experiment

---
Introduction
Investigation of the dynamic contact angle in a small capillary
Measurement of the contact line height, contact angle and pressure in the tank over time when a pressure step is given
Derivation of an ordinary differential equation (ODE) from a model
Start by taking the momentum equation
Comparison with the model given by Levine

---
Assumptions
- Symmetric flow in a rectangular channel
- No pressure losses at the inlet
- The height of the contact line is roughly equal to the height of the interface
- Poiseuille flow in the entire column

---
Derivation of the ODE (1/5)
- Start with the momentum equation
- Symmetric flow in one direction allows for a projection onto h-axis
  where	Is the mass of the column
- The Forces can be written as follows
[Speaker Notes: \frac{\text{d}}{\text{dt}}\left(m \dot{\vec{v}}\right) = \sum_i \vec{F_i} \frac{\text{d}}{\text{dt}}\left(m \dot{h}\right) = \sum_i {F_i} m = \rho L \delta h \sum_i F_i = F_{St} + F_{g} + F_{\Delta p}+ F_{visc}]

---
Derivation of the ODE (2/5)
- The surface tension force can be written as
  where is the perimeter of the channel
- The gravitational force can be written as
  where is once again the mass of the liquid column
- The force due to pressure is given by
  where is the area of the channel
- The viscous force is calculated via the shear stress
  where we assume the wetted area to be
[Speaker Notes: F_{st} = \sigma P \text{cos}\Theta P = 2(L + \delta) F_g = - m g m = \rho L \delta h F_{\Delta p} = \Delta p A A = \delta L F_\text{visc} = A_\text{wet} \tau A_\text{wet} = 2 (\delta + L) h]

---
Derivation of the ODE (3/5)
- The parabolic profile is given by
- This leads to the shear stress
- Relate the maximum to the mean velocity by integrating over the width of the channel
[Speaker Notes: u(y) = u_\text{max} \left(1 - \frac{y^2}{(\delta/2)^2}\right) \tau &= \mu \frac{\text{d}u}{\text{d}y} \bigg\rvert_{y = \delta/2} = - 2 \mu u_\text{max} \frac{y}{(\delta/2)^2} \bigg\rvert_{y = \delta/2} = -4 \frac{\mu u_\text{max}}{\delta}]

---
Derivation of the ODE (4/5)
- The conservation of mass leads to
- The viscous force can now be expressed as
[Speaker Notes: \bar{u} &= \frac{1}{\delta} \int_{-\delta/2}^{\delta/2} u_\text{max} \left(1 - \frac{y^2}{(\delta/2)^2}\right) = \frac{1}{\delta} u_\text{max} \left(y - \frac{y^3}{3(\delta/2)^2}\right)\bigg\rvert_{y = -\delta/2}^{\delta/2} = \frac{1}{\delta} u_\text{max} \left(\delta - \frac{\delta}{3}\right) = \frac{2}{3}u_\text{max} F_\text{visc} = 2 (L+\delta) h \tau = - 12 \frac{(L + \delta) \mu}{\delta} h\dot{h}]

---
Derivation of the ODE (5/5)
- The inertia term can be written as
- Everything together yields the desired ODE
- Dividing by and rearranging yields
[Speaker Notes: \frac{\text{d}}{\text{dt}}\left(\rho L \delta h \dot{h}\right) = \rho L \delta \left(\dot{h}^2 + \ddot{h}h\right) \rho L \delta \left(\dot{h}^2 + \ddot{h}h\right) = 2(L + \delta) \sigma \text{cos}\Theta + \Delta p L \delta - \rho g L \delta h - 12 \frac{\mu (L + \delta)}{\delta} \dot{h}{h} \ddot{h}h + \dot{h}^2 + g h + 12 \frac{\mu (L + \delta)}{\rho \delta^2 L} \dot{h}{h} = \frac{2(L + \delta) \sigma}{\rho L \delta} \text{cos}\Theta + \frac{\Delta p}{\rho}]

---
Comparison
- Levine model for a circular tube
- Own derivation for a rectangular channel
- The Levine model considers pressure losses at the inlet
- Differences can be made up for by using corrective factors for some coefficients
- The pressure term is added as we are looking at the oscillation and not just the rise
[Speaker Notes: \rho R^2 \left(\left(h + \frac{37}{36}R\right) \ddot{h} + \frac{7}{6} \dot{h}^2\right) = 2R \sigma \text{cos}\Theta - 8 \mu h \dot{h} - \rho R^2 g h - \frac{2 \rho R^2 \mu}{\rho a} \dot{h}]