Introduction
Investigation of the dynamic contact angle in a small capillary
Measurement of the contact line height, contact angle and pressure in the tank over time when a pressure step is given
Derivation of an ordinary differential equation (ODE) from a model
Start by taking the momentum equation
Comparison with the model given by Levine

---
Sketch of the experiment

---
Derivation of the ODE (1/4)
- Start with the momentum equation
- Assuming symmetry and a flow only along the height
  where	Is the mass of the column
- The Forces can be written as follows
[Speaker Notes: \frac{\text{d}}{\text{dt}}\left(m \dot{\vec{v}}\right) = \sum_i \vec{F_i} \frac{\text{d}}{\text{dt}}\left(m \dot{h}\right) = \sum_i {F_i} m = \rho L \delta h \sum_i F_i = F_{St} + F_{g} + F_{\Delta p}+ F_{visc}]

---
Derivation of the ODE (2/4)
- The first three can be written without further derivation as
  , the force due to surface tension
  , the force due to gravity
  , the force due to the given pressure difference
- The viscous term requires a closer look
- Assume a Poiseuille flow in a rectangular channel
- Neglecting the extension of the profile into the x we get the profile
[Speaker Notes: F_{St} = 2 \sigma (\delta + L) \text{cos}\Theta F_g = - \delta L h \rho g F_{\Delta p} = \Delta p \delta L u(y) = u_\text{max} \left(1 - \frac{y^2}{(\delta/2)^2}\right)]

---
Derivation of the ODE (3/4)
- We can express this as a term of the mean velocity by integrating
- The mean velocity can be roughly estimated as the velocity of the fluid
- Now we can calculate the wall shear stress
- And the resulting force
[Speaker Notes: \bar{u} = \frac{1}{\delta} \int_{-\delta/2}^{\delta/2} u_\text{max} \left(1 - \frac{y^2}{(\delta/2)^2}\right) \text{d}y = \frac{2}{3} u_\text{max} \bar{u} \approx \dot{h} \tau = \mu \frac{\text{d}u}{\text{d}y} \bigg\rvert_{\delta/2} = - 6 \frac{\mu \dot{h}}{\delta} F_\text{visc} = 2 (L+\delta) h \tau = - 12 \frac{(L + \delta) \mu}{\delta} h\dot{h}]

---
Derivation of the ODE (4/4)
- The inertia term can be written as
- Everything together yields the desired ODE
- Eliminating the prefactor and rearranging yields
[Speaker Notes: \frac{\text{d}}{\text{dt}}\left(\rho L \delta h \dot{h}\right) = \rho L \delta \left(\dot{h}^2 + \ddot{h}h\right) \rho L \delta \left(\dot{h}^2 + \ddot{h}h\right) = 2(L + \delta) \sigma \text{cos}\Theta + \Delta p L \delta - \rho g L \delta h - 12 \frac{\mu (L + \delta)}{\delta} \dot{h}{h} \ddot{h}h + \dot{h}^2 + g h + 12 \frac{\mu (L + \delta)}{\rho \delta^2 L} \dot{h}{h} = \frac{2(L + \delta) \sigma}{\rho L \delta} \text{cos}\Theta + \frac{\Delta p}{\rho}]

---
Comparison
- Levine model for a circular tube
- Own derivation for a rectangular channel
- The Levine model considers pressure losses at the inlet
- Differences can be made up for by using corrective factors for some coefficients
[Speaker Notes: \rho R^2 \left(h + \frac{37}{36}R\right) \ddot{h} = 2R \sigma \text{cos}\Theta - 8 \mu h \dot{h} - \rho R^2 g h - \frac{1}{2} \rho R^2 \left(\frac{7}{3} \dot{h}^2 + \frac{4 \mu}{\rho a} \dot{h} \right)]