Sketch of the experiment

---
Introduction
Investigation of the dynamic contact angle in a small capillary
Measurement of the contact line height, contact angle and pressure in the tank over time when a pressure step is given
Derivation of an ordinary differential equation (ODE) from a model
Start by taking the momentum equation
Comparison with the model given by Levine

---
Assumptions
Symmetric flow in a rectangular channel
No pressure losses at the inlet
The height of the contact line is roughly equal to the height of the interface
Poiseuille flow in the entire column
Velocity profile in the x-direction is uniform

---
Derivation of the ODE (1/5)
Start with the momentum equation
Symmetric flow in one direction allows for a projection onto z-axis
Where	Is the mass of the column
The Forces can be written as follows
[Speaker Notes: \frac{\text{d}}{\text{dt}}\left(m \dot{\vec{v}}\right) = \sum_i \vec{F_i} \frac{\text{d}}{\text{dt}}\left(m \dot{h}\right) = \sum_i {F_i} m = \rho L \delta h \sum_i F_i = F_{St} + F_{g} + F_{\Delta p}+ F_{visc}]

---
Derivation of the ODE (2/5)
The surface tension force can be written as
where is the perimeter of the channel
The gravitational force can be written as
where is once again the mass of the liquid column
The force due to pressure is given by
where is the area of the channel
The viscous force is calculated via the shear stress
where we assume the wetted area to be
[Speaker Notes: F_{st} = \sigma P \text{cos}\Theta P = 2(L + \delta) F_g = - m g m = \rho L \delta h F_{\Delta p} = \Delta p A A = \delta L F_\text{visc} = A_\text{wet} \tau A_\text{wet} = 2 (\delta + L) h]

---
Derivation of the ODE (3/5)
The parabolic profile is given by
This leads to the shear stress
Relate the maximum to the mean velocity by integrating over the width of the channel
[Speaker Notes: u(y) = u_\text{max} \left(1 - \frac{y^2}{(\delta/2)^2}\right) \tau &= \mu \frac{\text{d}u}{\text{d}y} \bigg\rvert_{y = \delta/2} = - 2 \mu u_\text{max} \frac{y}{(\delta/2)^2} \bigg\rvert_{y = \delta/2} = -4 \frac{\mu u_\text{max}}{\delta}]

---
Derivation of the ODE (4/5)
The conservation of mass leads to
The viscous force can now be expressed as
[Speaker Notes: \bar{u} &= \frac{1}{\delta} \int_{-\delta/2}^{\delta/2} u_\text{max} \left(1 - \frac{y^2}{(\delta/2)^2}\right) = \frac{1}{\delta} u_\text{max} \left(y - \frac{y^3}{3(\delta/2)^2}\right)\bigg\rvert_{y = -\delta/2}^{\delta/2} = \frac{1}{\delta} u_\text{max} \left(\delta - \frac{\delta}{3}\right) = \frac{2}{3}u_\text{max} F_\text{visc} = 2 (L+\delta) h \tau = - 12 \frac{(L + \delta) \mu}{\delta} h\dot{h}]

---
Derivation of the ODE (5/5)
The inertia term can be written as
Everything together yields the desired ODE
Dividing by and rearranging yields
[Speaker Notes: \frac{\text{d}}{\text{dt}}\left(\rho L \delta h \dot{h}\right) = \rho L \delta \left(\dot{h}^2 + \ddot{h}h\right) \rho L \delta \left(\dot{h}^2 + \ddot{h}h\right) = 2(L + \delta) \sigma \text{cos}\Theta + \Delta p L \delta - \rho g L \delta h - 12 \frac{\mu (L + \delta)}{\delta} \dot{h}{h} \ddot{h}h + \dot{h}^2 + g h + 12 \frac{\mu (L + \delta)}{\rho \delta^2 L} \dot{h}{h} = \frac{2(L + \delta) \sigma}{\rho L \delta} \text{cos}\Theta + \frac{\Delta p}{\rho}]

---
Comparison
Levine model for a circular tube
Own derivation for a rectangular channel
The Levine model considers pressure losses at the inlet
Differences can be made up for by using corrective factors for some coefficients
The pressure term is added as we are looking at the oscillation and not just the rise
[Speaker Notes: \rho R^2 \left(\left(h + \frac{37}{36}R\right) \ddot{h} + \frac{7}{6} \dot{h}^2\right) = 2R \sigma \text{cos}\Theta - 8 \mu h \dot{h} - \rho R^2 g h - \frac{2 \rho R^2 \mu}{\rho a} \dot{h}]